## Slide 1: Modelling and Simulation of Environmental Disturbances (Module 5)
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Dr Tristan Perez
Centre for Complex Dynamic Systems and Control (CDSC)
Prof. Thor I Fossen
Department of Engineering Cybernetics
Notes: <number>

## Slide 2: Regular waves in deep water
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The sea surface elevation is described by:
where
Wave number
(rad/m)
Wave length
(m)
Phase velocity
(m/sec)
These expressions are only valid in deep water
, where h is the water depth.
Wave frequency
(rad/s)
Notes: <number>

## Slide 3: Sailing condition
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The sailing condition of a vessel is given by its forward speed U and its encounter angle, i.e., the heading angle relative to the waves.
Encounter angle
Notes: <number>

## Slide 4: Encounter frequency
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
If the waves are observed from a reference frame that moves at a constant speed, the frequency observed is called Encounter Frequency.
This is a Doppler effect
Negative encounter frequency => vessel overtakes the waves
Notes: <number>

## Slide 5: Ocean waves
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Ocean waves present, in general, irregularity in time and space and cannot be predicted exactly: Stochastic Process.
t
ζ(0,0,t)
ζ(x,y,0)
Notes: <number>

## Slide 6: Stochastic sea description
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
In practice, it is assumed that the variations of a stochastic nature of the sea are much slower than the variations of the sea surface itself; Hence,
ζ(x, y, t) can be considered a realization of a stationary and homogeneous stochastic process.
For deep water waves, ζ(x, y, t) is further assumed Gaussian.
Notes: <number>

## Slide 7: Gaussian waves
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The elevation of the sea surface can be thought as being generated as the sum of many sinusoidal waves with different amplitudes, frequencies, and phases.
ζ(x,y,0)
t
ζ
p(ζ)
ζ(xo,yo,t)
(xo,yo)
Notes: <number>

## Slide 8: How good are these hypotheses?
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
From data collected at sea (Haverre & Moan, 1985), it can be stated that
For low and moderate seas (H1/3 < 4m), the sea can be considered stationary for periods over 20 min. For more severe sea states, stationarity can be questioned even for periods of 20 min.
For medium seas (4m < H1/3 < 8m), Gaussian models are still accurate, but deviations from Gaussianity slightly increase with the increasing severity of the sea state.
If the water is sufficiently deep, wave elevation can be consider Gaussian regardless of the sea state.
(H1/3 is the average of the highest one third of the waves recorded.)
Notes: <number>

## Slide 9: Random sea characterization
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Under the Gaussianity assumption, the process is completely described by
Mean
Variance
The sea surface elevation is described relative to the mean free surface; therefore, the mean of the SP is zero.
The variance is described in terms of a sea power spectral density or sea spectrum.
Notes: <number>

## Slide 10: Power spectral density definition
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
If we use the frequency in Hz to define the FT, then
and
from which the name power spectral density follows.
This definition is common in the literature of electrical communications and signal processing.
Notes: <number>

## Slide 11: PSD alternative definition
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
When we use the circular frequency (rad/s) to define the FT,
We need to be careful on how we compute power!!!
Notes: <number>

## Slide 12: Random sea characterization
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The spectral moments of order n are defined as:
Then the variance and standard deviation (RMS value) are
 =
Notes: <number>

## Slide 13: Statistics of wave period
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 14: Narrow and wide banded processes
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 15: Example narrow and wide-banded
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Narrow-banded signal
Wide-banded signal
Notes: <number>

## Slide 16: Statistics of wave height
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 17: Statistics of Maxima
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 18: Long- and short-crested Seas
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
After the wind has blown constantly for a certain period of time, the sea elevation can be assumed statistically stable. In this case, the sea is referred to as fully-developed.
If the irregularity of the observed waves are only in the dominant wind direction, so that there are mainly uni-directional wave crests with varying separation but remaining parallel to each other, the sea is referred to as a long-crested irregular sea.
When irregularities are apparent along the wave crests at right angles to the direction of the wind, the sea is referred to as short crested or confused sea.
Notes: <number>

## Slide 19: Long-crested Seas
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 20: Short-crested Seas
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 21: Idealised spectra Long-crested seas
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
In cases where no wave records are available, standard, idealized, formulae can be used. One family of idealized spectra is the Bretschneither family which was developed in early 1950s:
(This family can be used to represent rising and falling seas, as well as fully developed seas with no swell and unlimited fetch.)
Modal frequency
Spectral moments
Notes: <number>

## Slide 22: Idealised Spectra
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
In the 1960’s, the Pierson-Moskowitz family was developed to forecast storm waves at a single point in fully developed seas with no swell using wind data. This family relates the parameters A and B to the
average wind speed at 19.5m above the sea surface:
The ITTC recommends the use of the Modified Pierson-Moskowitz family; significant wave height and zero-crossing period or the average wave period is used:
Notes: <number>

## Slide 23: Example ITTC spectra
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 24: Other Spectra seas
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Other families:
The JONSWAP spectral family accounts for the case of limited fetch wind waves
The TMA spectral family is an extension of the JONSWAP for finite water depth,
The double-peak Torsethaugen spectral family accounts for both swell and wind waves,
The Ochi six-parameter spectral family can be fitted to almost any wave record (it could account for swell and wind waves.)
For further details see Ochi, K. (1998) Ocean Waves: The Stochastic Approach, Cambridge University Press. Ocean Tech. Series.
Notes: <number>

## Slide 25: Spectra for Short-crested Seas
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Directional spectra are more realistic and are very important to calculate loads on marine structures since the motion response depends highly on the encounter angle. For simulation, it is common to separate the directional spectrum as a product of two functions:
is the spreading function
Notes: <number>

## Slide 26: Spreading Function
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
where χ0 is the dominant wave propagation direction, and the values of s = 1, 2 are commonly used. See Lloyd (1989) for a more general form where |χ − χ0| < α; with α not necessarily equal to π/2
Notes: <number>

## Slide 27: Time-domain Simulations
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
If ζ(t) is stationary and Gaussian on time interval [0, T], its realizations can be approximated to any degree of accuracy by
with N sufficiently large; where σn are constants and the phases εn are independent identically distributed random variables with uniform distribution in [0, 2π].
The autocorrelation is given by
Notes: <number>

## Slide 28: Time-domain Simulations
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 29: Why is it done this way?
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 30: Formulae for Time-damin Simulations
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 31: Wind
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Wind is commonly divided in two components; a mean value and a fluctuating component, or gust.
The mean component decreases with the distance towards the ground or the surface of the ocean, whereas the gust is approximately constant with the distance to the ground or the surface of the ocean—boundary layer.
It is a 3D phenomenon, but in marine applications we restrict it to 2D, and velocities are considered only in the horizontal plane.
Wind is parameterized by the velocity U and the direction ψ. The direction is taken with respect to the North-East.
Note that, in general, the direction of the wind is the direction from where the wind is coming from, e.g., a SE wind blows from the SE towards NW.
Notes: <number>

## Slide 32: Wind Mean-velocity Component
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Slowly-varying fluctuations in the mean wind velocity can be modeled by a 1st order Gauss-Markov Process:
where w is Gaussian white noise and μ ≥ 0 is a constant.
The magnitude of the velocity should be restricted by saturation elements
Notes: <number>

## Slide 33: Wind Mean-direction component
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Slowly-varying fluctuations in the mean wind direction can also be implemented by a 1st order Gauss-Markov Process (Sorensen, 2005):
The direction is taken with respect to the (n-frame).
NOTE: This direction is often the direction from where the wind is blowing: North-East (NE) wind blows from the NE
Notes: <number>

## Slide 34: Wind velocity and direction
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Sorensen, (2005)
Notes: <number>

## Slide 35: Wind Gust
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The wind gust is model as a realization of a stochastic process with a particular spectrum (Sorensen, 2005).
Notes: <number>

## Slide 36: Current
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Current velocity magnitude:
Current direction:
The direction is taken with respect to the (n-frame). NOTE: This direction is the direction to where the current flows : North-East (NE) current flow towards the NE. (This is different from the convention for wind)
Surface Current
Notes: <number>

## Slide 37: References
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Perez, T. (2005) Ship Motion Control. Springer.
Ochi, M. (2005) Ocean Waves: the stochastic approach. Cambridge University Press.
Sorensen, A.J. (2005) “Marine Cybernetics.” Lecture notes, Dept. of Marine Technology NTNU, NORWAY.
Notes: <number>