## Slide 1: Seakeeping Models in the Frequency Domain (Module 6)
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Dr Tristan Perez
Centre for Complex Dynamic Systems and Control (CDSC)
Prof. Thor I Fossen
Department of Engineering Cybernetics
Notes: <number>

## Slide 2: Linear hydrodynamic forces in waves
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Linear theory can describe hydrodynamic loads to a great extent in low to medium sea states (depending on the size of the ship)
Linear means that the loads and the motion are proportional to the wave amplitudes.
Linearity means superposition: the loads and responses due to irregular seas can be obtained by linear combination of responses to regular or sinusoidal seas.
Also due to the linearity assumption, the study can be performed either in time or frequency domain.
Notes: <number>

## Slide 3: Linear hydrodynamic forces
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
LinearLoads
Linear eq of motion
waves
Motion
Some of the loads depend on the excitation due to the waves, while other depend on the motion of the vessel itself.
The second type of loads give the system a feedback structure.
Notes: <number>

## Slide 4: Adding nonlinear forces
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Once we have a linear time-domain model, nonlinear loads can be added due to the assumption of force superposition:
LinearLoads
Linear eq of motion
waves
Motion
Loads
Nonlinear Loads
So, the linear model should not be seen as a limitation; rather as a basis upon which we can build nonlinear models based on the assumption of force superposition.
Notes: <number>

## Slide 5: Linear hydrodynamic analysis
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Due to linearity, we can study the problem for sinusoidal excitation and then use these results to obtain solutions to non-sinusoidal cases via superposition.
The hydrodynamic problem of obtaining loads and motion for sinusoidal waves can be separated into two sub-problems:
Excitation problem: The ship is restrained from moving and kept in its mean position, and the excitation loads are obtained as a result of changes in pressure due to the incoming waves.
Radiation problem: The ship is forced to oscillate in calm water in each DOF with a frequency equal to the wave excitation frequency.
Notes: <number>

## Slide 6: Radiation forces
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Radiation loads appear due to the motion of the ship—the change in momentum of the fluid due to the motion of the hull changes the pressure on the hull, which induce the loads.
These loads have two components
  Proportional to the accelerations
  Proportional to the velocities
Notes: <number>

## Slide 7: Radiation forces
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
free surface condition (dynamic+kinematic conditions)
Boundary conditions:
sea bed condition
dynamic body condition
radiation condition
Regular outgoing waves
are observed at large distance from the vessel
Notes: <number>

## Slide 8: Computing forces
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Forces and moments are obtained by integrating the pressure over the average wetted surface Sw:
Radiation forces and moments:
DOF:
1-surge
2-sway
3-heave
4-roll
5-pitch
6-yaw
Notes: <number>

## Slide 9: Radiation forces for regular motion
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
If the motion of the vessel on the DOF i is harmonic:
Then, after integrating the pressure over the surface of the hull, the radiation forces in the DOF j due to the motion in the DOF i take the following form:
← Only in steady state condition.
Notes: <number>

## Slide 10: Radiation forces for regular motion
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The coefficients that multiply the accelerations are called added mass coefficients even though not all of them have units of mass. The added mass terms give the forces due to the accelerations of the fluid as the vessel oscillations—the whole fluid will oscillate with different fluid particle amplitudes.
The coefficients proportional to the velocities are called potential damping coefficients. The potential damping terms represent the energy carried away by the waves generated due to the motion of the hull.
Notes: <number>

## Slide 11: Added mass and damping
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Example of added mass and potential damping in heave of a symmetric rectangular barge 8x4x45m:
The added mass and damping coefficients depend on
Shape of the hull
Forward speed
Water depth
Notes: <number>

## Slide 12: Symmetry
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
There is a total of 36 added mass and 36 damping coefficients.
If the structure has zero speed and a plane of symmetry, half of the coefficients are zero. (for this to hold with forward speed, the plane of symmetry has to be parallel to the forward direction.)
If the structure has zero speed and there is no current, then the matrices of added mass and damping are symmetric:
Notes: <number>

## Slide 13: Restoring forces (linear)
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The resotring forces are due to changes in displacement:
(Awp waterplane area)
These are computed for calm water—Calm water stability.
Notes: <number>

## Slide 14: Linear Wave Excitation
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The linear wave excitation or 1st order waves excitation are the loads on the structure when it is restrained from oscillating and there are incident waves. The linear assumption assumes the loads are proportional to the wave amplitude.
1st order wave loads are separated into two components:
  Froude-Kriloff
  Diffraction
Notes: <number>

## Slide 15: Froude-Kriloff loads
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The Froude-Kriloff loads are obtained by integrating the pressure due to undisturbed wave field over the mean wetted surface of the body—It is assumed that the body does not disturb the wave field.
These can be considered within a nonlinear framework by integrating over the instantaneous wetter surface.
Notes: <number>

## Slide 16: Diffraction loads
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The diffraction loads appear due to the change in the wave field by the presence of the body.
These can be computed in a similar way as the radiation forces by considering a BVP; the main difference is that the boundary condition on the body:
  The velocity due to the diffraction potential has to be equal and opposite to the velocity due to undisturbed wave potential.
  This body condition ensures there will be no fluid transport through the body.
Notes: <number>

## Slide 17: RAOS—Frequency response functions
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Sea surface elevation
Force RAO
combined
Motion RAO
motion
Force to Motion RAO
Notes: <number>

## Slide 18: Force RAO
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
For a regular wave
The linear excitation forces will be
The amplitude and phase of the excitation force depend on
Wave Frequency
Encounter angle
Wave amplitude
Forward speed
Notes: <number>

## Slide 19: Force RAO
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Example heave Force RAO (i=3) for a barge (8x4x45m):
Notes: <number>

## Slide 20: Motion RAO
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Example motion Force RAO (i=3) for a barge (8x4x45m):
Notes: <number>

## Slide 21: Force to motion FRF
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Using the added mass and damping with the linear (seakeeping) equation of motion we can obtain the force to motion frequency response function:
This is sometimes written in the hydrodynamic literature as
This is an abuse of notation since this is not a true equation of motion; it is a different (rather confusing) way to write the frequency response function.
Notes: <number>

## Slide 22: Force to motion FRF
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Then we can define the force to motion frequency response matrix:
Notes: <number>

## Slide 23: Motion RAO
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The Force RAO relates the wave elevation to the linear excitation forces.
By combining the Force RAO with the Force to motion frequency response matrix we obtain the motion frequency response due to wave elevation or Motion RAO:
Notes: <number>

## Slide 24: Statistics of Loads and Motion
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Since the wave elevation is assumed a zero-mean Gaussian process and the system is assumed linear, the loads and the response are also zero-mean and Gaussian processes.
The spectra of loads and response is all that is needed to compute any statistics:
Notes: <number>

## Slide 25: Simulation of wave loads and motion time series
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Having the spectrum, we can simulate time series of loads and motion in the same way we do it for the wave elevation:
-uniformly distributed in [0,2]
Notes: <number>

## Slide 26: Non-linear wave loads
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
There are some problems related to wave-structure interactions which cannot be described by linear Theory alone.
The nonlinear problems attempt to describe more accurately the free-surface and body conditions on the instantaneous rather than mean values.
A convenient way to solve nonlinear wave-structure problems is by using perturbation analysis.
In a second order theory, the problems are solved up second-order in incident wave amplitude—i.e., in the potential and pressure terms proportional to the wave amplitude and wave amplitude square are considered.
Notes: <number>

## Slide 27: Non-linear wave loads
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The effects of second-order loads are important for structures which are kept in position by mooring lines, anchors, and propulsion systems, and for vessels following trajectories.
The solution of a second order problem evidences
Mean wave drift force
Slowly-varying wave drift force (sub harmonic)
Rapidly varying wave drift force (super harmonic)
Notes: <number>

## Slide 28: Evidence of second-order loads
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
A simple way to evidence the effects of a second order problem is to look at the quadratic term in the Bernoulli equation:
Then,
Notes: <number>

## Slide 29: Evidence of second-order loads
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Consider the case where
Then,
Mean components
Slowly varying component
rapidly varying components
These give rise to 2nd order pressure force components!
Notes: <number>

## Slide 30: Non-linear wave load effects
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Mean wave-drift force: Determine the equilibrium position of the moored system (together with wind and current). They are important for the design of mooring lines and propulsion systems for dynamic positioning.
Slowly-varying wave-drift force: The forces have frequencies much slower than the wave elevation. These can excite resonant modes in the horizontal position of the moored vessel. Typical resonance periods in offshore structures are 1 to 2min.
Rapidly-varying wave-drift force: these forces have frequency components which are higher than the wave elevation frequency. These can excite structural resonant modes: periods 2 to 4s.
Notes: <number>

## Slide 31: Example (Pinkster 1979)
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 32: Second order FRF
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
For slowly varying wave-drift forces, the second order potential is needed.
With the second order potential, the second order FRF be computed:
Notes: <number>

## Slide 33: Mean wave drift from 2ord FRF
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Note that
Then the mean wave drift forces can ne obtained from:
Notes: <number>

## Slide 34: Hydrodynamic Codes
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The working principle of all codes:
Code
Input data and
Pre-processing
Hull geometry
Loading condition
Environment (frequencies)
Calculation settings
A(w), [A(∞)]
B(w), [B(∞)]
1st order force FRF
2nd order force FRF
Motion FRF
Output data and
Post-processing
Notes: <number>

## Slide 35: References
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Faltinsen, O.M. (1990) Sea Loads on Ships and Ocean Structures. Cambridge University Press.
Journée, J.M.J. and W.W. Massie (2001) Offshore Hydromechanics. Lecture notes on offshore hydromechanics for Offshore Technology students, code OT4620. (http://www.ocp.tudelft.nl/mt/journee/)
Perez, T. and T. I. Fossen (2006) “Time-domain Models of Marine Surface Vessels Based on Seakeeping Computations.” 7th IFAC Conference on Manoeuvring and Control of Marine Vessels MCMC, Portugal, September.
Notes: <number>