## Slide 1: Time-domain models based on frequency-domain data (Module 7)
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Dr Tristan Perez
Centre for Complex Dynamic Systems and Control (CDSC)
Prof. Thor I Fossen
Department of Engineering Cybernetics
Notes: <number>

## Slide 2: Time-domain modelling approaches
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Two approaches can be distinguished for time-domain modelling:
Full time-domain hydrodynamic codes,
Time-domain models based on frequency-domain data.
Here, we will follow the second approach.
Notes: <number>

## Slide 3: Linear time-domain models
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Linear time-domain models can be used for control system design and can serve as a basis for developing non-linear models:
Linear model
Motion
Nonlinearities
Loads
Wave Loads
Notes: <number>

## Slide 4: Frequency-domain Eq. of Motion
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
In the hydrodynamic literature it is common to find
This is valid to describe the steady-state response to sinusoidal excitations.
This is a false time-domain model; it is simply an alternative (and confusing) way to write the frequency response of the system (Cummins, 1962).
Notes: <number>

## Slide 5: Cummins’s equation
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Cummins (1962), took a different modelling approach and consider the radiation problem ab initio in the time domain. He obtained the Cummins’s equation of motion:
The added mass matrix is constant—frequency and speed independent.
The convolution term accounts for fluid-memory effects.
The kernel of the convolution is a matrix of retardation functions or impulse responses.
This is a true linear equation of motion, and it is valid for any excitation, provided the linearity assumption holds.
Notes: <number>

## Slide 6: Cummins’s equation with forward speed
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The convolution terms depend on the forward speed.
With forward speed appears a constant damping term.
The restoring forces are affected by hydrodynamic pressure—Lift, changes in trim. (Usually ignored for Fn<0.3)
Notes: <number>

## Slide 7: Ogilvie’s relations
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
From the Riemann-Lesbesgue Lemma:
If Cummins’s Equation is valid for any input, it must then be valid for sinusoids in particular (Ogilvie, 1964).
Ogilvie (1964) transformed the Cummins’ Equation to the frequency domain, and found that
Notes: <number>

## Slide 8: Time- and Freq-domain Relationships
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Frequency-domain relationship:
Time-domain relationship:
Notes: <number>

## Slide 9: Properties of the convolution terms
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The convolution terms have the following frequency and time-domain properties (e.g., Damaren, 2000):
 | Kij(s) have a zero at s=0
 | Strictly proper
 | Relative degree 1
 | BIBO stable
 | K(s) is passive => diagonal terms are positive real.
Notes: <number>

## Slide 10: Convolution replacement
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The convolution in the Cummins equation can be time and memory consuming for simulation. Simulations can be 40-times faster (Taghipour et.al, 2007a).
For analysis and design of a control system, the convolutions are not very well suited.
A state-space representation or appropriate order (n-order) eliminates the above problems:
Notes: <number>

## Slide 11: Convolution replacement
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Note that Dc=0 due to the relative degree 1.
Notes: <number>

## Slide 12: Convolution replacement
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The convolution replacement can be posed in different ways, which in “theory” should provide the same answer:
Time-domain
identification
Frequency-domain
identification
In practice one method can be more favourable than the other.
Model
conversion
Notes: <number>

## Slide 13: Identification problems
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Different proposals have appeared in the literature:
Time-domain identification:
LS-fitting of the impulse response (Yu & Falnes, 1998)
Realization theory (Kristiansen & Egeland, 2003)
Frequency-domain identification:
LS-fitting of the frequency response (Jeffreys, 1984),(Damaren 2000).
LS-fitting of added mass and damping (Soding 1982), (Xia et. al 1998), (Sutulo & Guedes-Soares 2006).
Notes: <number>

## Slide 14: Time-domain identification
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
From K(t) to state-space models.
Notes: <number>

## Slide 15: Numerical computations
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
A key issue for time-domain identification is to start with a good impulse response computed from the damping.
Numerical codes can only provide accurate computations of added mass and damping up to a certain frequency, say 
This introduces an error in the computation of the retardation functions:
Notes: <number>

## Slide 16: High-frequency values of A() and B()
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
In the limit at high frequency the following tendencies are observed for the 3D damping and added mass:
As commented by Damaren (2000), this seems at odds with what is generally stated in the hydrodynamic literature!
Note that there are no expansions involved to obtain these results, the only assumption is the linearity which results in a rational representation and the relative degree 1, which results from the integration of damping over the frequencies.
Notes: <number>

## Slide 17: Example Containership (Taghipour et al., 2007a)
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The panel sizing was done to be able to compute frequencies up to 2.5 rad/s.
Rule of thumb: characteristic panel length < 1/8 min wave length (Faltinsen, 1993).
Notes: <number>

## Slide 18: Numerical computations
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Extending the damping with tail prop to 1/2
In this example, the tail /2 is not a very good for B35 and B53 (2.5rad/s is too low), whereas it is ok for B33 and B55.
Notes: <number>

## Slide 19: Numerical computations
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Note the differences at t=0+, and the errors at different time instants.
When doing time-domain identification, it is important to start from a good approx of the retardation function!
Notes: <number>

## Slide 20: Impulse response curve fitting
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Given the SISO SS realization of order n:
The parameters can be obtained from
The application of this method to marine structures was proposed by Yu and Falnes (1998).
Notes: <number>

## Slide 21: Impulse response curve fitting
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
It is hard to guess the order of the system by looking at the impulse response alone—one should start with lower order and increase it to improve the fit.
The LS-problem is non-linear in the parameters. This problem can be solved with Gaussian-Newton methods.
The Gaussian-Newton methods are known to work well if the parameters’ initial guess are close to the optimal parameters.
Since the initial value of the parameters is difficult to obtain from the impulse response, and these depends on the particular realization being chosen, the method is not very practical.
Notes: <number>

## Slide 22: Realization theory
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
A key result of realization theory is the following factorization (Ho and Kalman, 1966):
Extended observability matrix
Extended controllability matrix
Hankel matrix of the impulse
response values (constant along
the anti-diagonals)
Notes: <number>

## Slide 23: Realization theory
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Kung’s Algorithm (Kung, 1978):
The number of significant
singular values give the order
of the system:
Singular value decomposition
Notes: <number>

## Slide 24: Realization theory
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Kung’s Algorithm (Kung, 1978):
The application of this method to marine structures was proposed by Kristiansen and Egeland (2003).
Notes: <number>

## Slide 25: Realization theory
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The problem is solved in discrete time
Kung’s algorithm obtains the model based on a SVD-factorization of the Hankel matrix of samples of the impulse response.
If the data is noisy or there are errors, it may not be quite clear to determine the order of the system from the singular values.
The conversion from discrete to continuous often gives a matrix Dc in the state-space realization, which is inconsistent with the dynamics of the problem for the retardation function (relative degree 1).
The MATLAB command imp2ss implements Kung’s algorithm, and chooses the order by neglecting singular values less than 1% of the largest one.
imp2ss requires using model order reduction afterwards (Kristiansen et al 2005).
The resulting models may not be passive.
Notes: <number>

## Slide 26: Example Container ship
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Singular values of the Hankel matrix of the samples of the impulse response.
These suggest (based on the blue plots)
Order K33(s) = 3 or 4
Oder K35(s) = 5 or 6
Order K55(s) = 3 or 4
Notes: <number>

## Slide 27: Example Container ship
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Impulse response fitting for K33(t) with a system of order 4.
Identification method: imp2ss + balmr (model order reduction).
K33(t)
K33(jw)
The identified model is not passive and does not have a zero at s=0.
Notes: <number>

## Slide 28: Example Container ship
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
K33(t)
K33(jw)
The identified model is passive, but still does not have a zero at s=0.
Impulse response fitting for K33(t) with a system of order 3.
Identification method: imp2ss + balmr (model order reduction).
Notes: <number>

## Slide 29: Example Container ship
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Impulse response fitting for K35(t) with a system of order 5.
K35(t)
K35(jw)
The identified model is passive, but still does not have a zero at s=0.
Note that the off-diagonal terms do not necessarily have to passive for K(s) to be passive (Unneland & Perez, 2007).
Notes: <number>

## Slide 30: Comments about Realization Theory
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Depending on the hydrodynamic data, it may be necessary to extend the damping at high freq. to have a good estimate the of the impulse response function before doing the idetification.
Looking at the impulse response fitting alone is not a good criteria—most properties are evident from the freq. response.
Imp2ss may require using model order reduction afterwards.
The models almost never satisfy the low frequency asymptotic values (zero at s=0).
High-order models may not be passive; this can solved trying different orders or using a model order reduction method that enforces passivity.
Notes: <number>

## Slide 31: Frequency-domain Identification
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
From K(j) to K(s)
Notes: <number>

## Slide 32: Regression in the frequency domain
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
In this method, a rational transfer function
is fitted to the frequency response data:
The application of this method to marine structures was proposed by Jeffreys (1984) and Damaren (2000).
Notes: <number>

## Slide 33: Quasi-linear regression
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Levi (1959) proposed the following linearization:
which is affine in the parameters and reduces to a linear LS problem.
This can be obtained If we chose the weights in the nonlinear problem as
Notes: <number>

## Slide 34: Iterative Quasi-linear regression
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The quasi-linear regressor tend to have a poor fit a low freq. This can be avoided by solving the linear LS problem iteratively, starting with the quasi-linear regressor and using the parameters obtained to compute a weighing:
After a few iterations, and the nonlinear problem is recovered.
Notes: <number>

## Slide 35: Minimum order transfer function
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Because of the zero at s=0 and the restriction of relative degree 1, the minimum order TF that can represent a convolution term is
Therefore, we can start with a system of order n=2, and then increase the order until we improve the fitting at an appropriate level.
Notes: <number>

## Slide 36: Containership example
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Frequency-domain identification of K33(jw) order 3
Identification method: iterative quasi-linear regression (invfreqs.m)
The model is passive and satisfy the asymptotic values.
Notes: <number>

## Slide 37: Containership example
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Frequency-domain identification of K35(jw) order 5 and K55(jw) order 3
Identification method: iterative quasi-linear regression (invfreqs.m)
Notes: <number>

## Slide 38: Reconstructing B()
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Notes: <number>

## Slide 39: Reconstructing A()
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
The model has good fitting at all frequencies.
Notes: <number>

## Slide 40: Comments about Freq.-dom. regression
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
FD-identification avoids having to compute the impulse response from the damping—thus, needing very high-frequency hydrodynamic data.
The identification method is simple: a series of linear LS problems—easy to programme.
The zero at s=0 and the relative degree can be enforced in the structure of the model, so the asymptotic values are always ensured.
The resulting models may be unstable: this is fixed by reflecting the unstable poles about the imaginary axis.
The resulting models may not be passive: this can be solved using weights in the LS problem.
Notes: <number>

## Slide 41: Simulink Model implementation
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
After obtaining a state-space representation or the transfers functions, we can assemble a complete model:
Notes: <number>

## Slide 42: References
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Perez, T. and T. I. Fossen (2006) “Time-domain Models of Marine Surface Vessels Based on Seakeeping Computations.” 7th IFAC Conference on Manoeuvring and Control of Marine Vessels MCMC, Portugal, September.
Perez, T. (2007) Identification and Validation of a Time-domain Hydrodynamic Model of a Prototype Hull for a Wave Energy Converter (WEC). Technical Report. Centre for Complex Dynamic Systems and Control. Australia.
Cummins, W., 1962. The impulse response function and ship motions. Schiffstechnik 9 (1661), 101–109.
Ogilvie, T., 1964. Recent progress towards the understanding and prediction of ship motions. In: 6th Symposium on Naval Hydrodynamics.
Kristiansen, E., Egeland, O., 2003. Frequency-dependent added mass in models for controller design for wave motion damping. In: Proceedings of 6th Conference on Maneoeuvering and Control ofMarine Craft, Girona, Spain.
Notes: <number>

## Slide 43: References
06/06/26
One-day Tutorial, CAMS'07, Bol, Croatia
<number>
Damaren, C.J. (2000). Time-domain floating body dynamics by rational approximations of the radiation impedance and diffraction mapping. Ocean Engineering 27, 687–705.
Yu, Z., Falnes, J., 1998. State-space modelling of dynamic systems in ocean engineering. Journal of Hydrodynamics B(1), 1–17.
Sutulo, S., Guedes-Soares, C., 2005. An implementation of the method of auxiliary state variables for solving seakeeping problems. International shipbuilding progress (Int. shipbuild. prog.) 52, 357–384.
Taghipour, R., Perez, T., Moan, T., 2007a. Hybrid Frequency-Time Domain Models for Dynamic Response Analysis of Marine Structures. (To appear in Ocean Engieering)
Taghipour, R., Perez, T., Moan, T., 2007b. Time domain hydroelastic analysis of a flexible marine structure using state-space models. In: 26th International Conference on Offshore Mechanics and Arctic Engineering-OMAE 07, San Diego, CA, USA.
Notes: <number>